Technical README: ROS2 IMU Publisher with MPU6050 on Jetson Orin
Introduction
This project enables the publication of calibrated IMU (Inertial Measurement Unit) data from an MPU6050 sensor to a ROS2 (Robot Operating System 2) topic. The setup utilizes a Jetson Orin module for processing, with the MPU6050 connected via I2C. The primary goal is to provide a calibrated IMU data stream for robotics, autonomous systems, or any application requiring precise motion sensing.
For the majority of applications focusing on short-term motion tracking, stabilization, or orientation estimation in dynamic environments, a 6-Axis IMU (accelerometer + gyroscope) provides a cost-effective, low-power, and sufficiently accurate solution. The addition of a magnetometer in 9-Axis IMUs is beneficial primarily in scenarios requiring absolute orientation in controlled magnetic environments or specific outdoor navigation challenges.
Working
1. Hardware Setup:
  1. MPU6050 IMU Sensor: Connected to the Jetson Orin via I2C.
  2. Jetson Orin Module: Runs the ROS2 node for publishing IMU data.
Jetson Orin	MPU 6050
Power pin 1	VCC
GND pin 6	GND
I2C5_DAT pin 3	SDA
I2C_CLK pin 5	SCL

1. Software Workflow:
  1. Initialization: Establish I2C connection and initialize the MPU6050.
  2. Calibration: Collect multiple IMU readings to calculate acceleration and gyroscope offsets.
  3. Data Publication: Periodically read IMU data, apply calibration offsets, and publish to a designated ROS2 topic.
Explanation of the Code
Dependencies
- adafruit_mpu6050 for MPU6050 interactions
- rclpy for ROS2 node management
- std_msgs.msg for ROS2 message types (specifically Float32MultiArray)
Key Components
IMUPublisher Class
- __init__ Method:
  - Initializes the ROS2 node named imu_publisher.
  - Sets up a publisher for the ros2_imu topic with a QoS (Quality of Service) depth of 10.
  - Creates a timer to trigger publish_imu_data every 1 second.
  - Initializes the I2C connection and the MPU6050 object.
  - Calls calibrate_sensor for initial calibration.
- calibrate_sensor Method:
  - Collects calibration_samples (default=100) of acceleration and gyroscope data.
  - Calculates the average offset for each axis.
  - Adjusts the Z-axis acceleration offset to account for gravity (assuming the sensor is stationary during calibration).
  - Logs the calculated offsets.
- publish_imu_data Method (Timer Callback):
  - Reads current acceleration, gyroscope, and temperature data from the MPU6050.
  - Applies the calibration offsets to the acceleration and gyroscope data.
  - Constructs a Float32MultiArray message with the calibrated data and temperature.
  - Publishes the message to the ros2_imu topic.
  - Optionally logs the published data to the console.
main Function
- Initializes the ROS2 environment.
- Creates an instance of the IMUPublisher node.
- Spins the node until a KeyboardInterrupt is detected.
- Properly destroys the node and shuts down the ROS2 environment upon exit.
Setup and Usage
1. Prerequisites:
  1. Jetson Orin with ROS2 installed.
  2. MPU6050 connected via I2C.
  3. Python dependencies installed (adafruit_mpu6050, rclpy, std_msgs).
2. Running the Node:
  1. Navigate to the project directory.
  2. Execute the script using Python (e.g., python3 mpu6050_calibrated.py).
3. Viewing Published Data:
  1. Use ROS2 tools (e.g., ros2 topic echo /ros2_imu) to view the published IMU data.
Troubleshooting
- Connection Issues: Verify I2C connection and MPU6050 address.
- Data Accuracy: Check calibration process and environmental factors.
- ROS2 Errors: Consult ROS2 logs and documentation for node or topic-related issues.
Future Development
- Enhanced Calibration: Implement more sophisticated calibration techniques for dynamic environments.
- Multi-Sensor Support: Expand to support additional IMU sensors or other types of sensors.
- Integration with Autonomous Applications: Utilize the published IMU data in robotics or autonomous vehicle projects.

Useful links:
Jetson pinout diagram for connection.