D2D using radar and ESP32 for collision avoidance.

Overview:
The project builds on a novel technique inspired by concepts from V2X and perceptive communication, implementing Device-to-Device (D2D) communication. In this communication framework, two entities exchange data simultaneously, wirelessly, and in real time over the 2.4 GHz frequency band. The core idea is to enable direct, low-latency communication between devices to share sensor data without relying on external networks.

This method, akin to Vehicle-to-Vehicle (V2V) communication in inter-vehicular networks, facilitates the exchange of critical information such as Cooperative Awareness Messages (CAM) and Decentralized Environmental Notification Messages (DENM). Such messages are vital for applications like collision avoidance and environmental awareness. In this implementation, onboard sensors send radar data, including Synthetic Aperture Passive Radar (SAPR) information and Euclidean distance measurements, which are crucial for tasks like collision prevention and 3D map generation.

By leveraging D2D communication, this setup ensures minimal latency, making it ideal for scenarios requiring fast data exchange and high responsiveness between entities, such as autonomous vehicle networks or robotic systems operating in dynamic environments.

Technical details:
 ESP32:
The ESP32, developed by Espressif, is a cost-effective and energy-efficient microcontroller family widely used in industry due to its flexibility and performance. In addition to standard WiFi and Bluetooth connectivity, it also supports ESP-NOW, a wireless communication protocol designed for direct micro controller-to-microcontroller communication.

Additionally, ESP-NOW is a connection-less protocol, allowing each device to pair with up to 20 other peers. The maximum payload size is 250 bytes, with a standard bit rate of 1 Mbps. Like WiFi, every device is assigned a unique MAC address for direct communication. For broadcast messaging, the designated address is 0xff:0xff:0xff:0xff:0xff:0xff.

IWR6843ISK:
The Texas Instruments IWR6843ISK mmWave radar sensor is employed to transmit Synthetic Aperture Passive Radar (SAPR) data periodically to the ESP32 microcontroller via a serial interface. The IWR6843ISK, based on the IWR6843 chip, is capable of sensing and processing a wide array of radar data, including range, elevation, signal-to-noise ratio (SNR), and timestamp information. This data is critical for various applications, such as object detection, tracking, and environmental mapping.
For interfacing with the ESP32, the IWR6843ISK transmits the processed radar data over a UART (Universal Asynchronous Receiver-Transmitter) connection. The UART protocol enables asynchronous, low-latency, and full-duplex serial communication, making it suitable for real-time radar data transfer. The ESP32, with its built-in WiFi and Bluetooth capabilities, can then further process or wirelessly transmit the radar data for external analysis or control

Standard UART :
The standard UART (Universal Asynchronous Receiver-Transmitter) interface was employed for communication between the ESP32 and the Jetson Orin board. Specifically, the ESP32 utilized its UART pins, which include RX (receive), TX (transmit), and GND (ground), to establish serial communication with the Jetson Orin board, where the same corresponding pins were used.

UART is a fundamental communication protocol in embedded systems that allows serial data transmission without requiring a clock signal. This asynchronous communication protocol relies on a predefined baud rate for synchronization, allowing data to be transferred in a start-stop format. In this system, the TX pin of the ESP32 transmits data to the RX pin of the Jetson Orin, while the GND pin ensures a common reference voltage between the two devices, preventing issues like voltage mismatches.

By leveraging UART, the system enables full-duplex communication, where the ESP32 can simultaneously send and receive data to and from the Jetson Orin board. This method is particularly advantageous for applications requiring simple and efficient point-to-point communication with minimal overhead, as UART does not require handshaking lines like more complex protocols (e.g., SPI or I2C).

Applications:
Application 1:
Collision avoidance using positional (Euclidean) values of two mobile robots.
In this application, positional data of two mobile robots is tracked via a Vicon motion capture system. The Vicon system provides high-precision Euclidean coordinates of the robots, which are then transmitted wirelessly to the ESP32 microcontroller. The ESP32 processes these coordinates and ensures that real-time updates are shared between the robots, enabling collision avoidance by analyzing relative distances and directions.

Application 2:
Perceptive communication using RADAR SAPR data and positional values.
In this scenario, the IWR6843ISK mmWave radar sensor sends Synthetic Aperture Passive Radar (SAPR)** data to the ESP32, which includes range, elevation, and other spatial parameters. Simultaneously, the Vicon tracker provides positional (Euclidean) values of two mobile robots. This integrated data, combining radar and motion capture information, is used for perceptive communication, enhancing situational awareness by providing both radar-based environmental sensing and precise positional updates for advanced coordination between robots.

Arduino:
The application used for programming is the Arduino 1.8.19 Legacy IDE.
It is always convenient to install Arduino application on the Host Pc and the corresponding libraries for debugging.
One can follow the following link to install the Arduino for the board esp32.
Although one can then run the arduino.ino files directly via the linux command terminal using Arduino CLI.

Steps to download and flash the Arduino code from the terminal:

1. Download the Arduino CLI:
  1. Run the following command to download the Arduino CLI:
    curl -fsSL https://raw.githubusercontent.com/arduino/arduino-cli/master/install.sh | sh
2. Add Arduino CLI to your PATH:
  1. After the installation, add the Arduino CLI binary to your system's PATH. You can do this by editing the ~/.bashrc file or ~/.zshrc (depending on your shell):
    nano ~/.bashrc # or nano ~/.zshrc for zsh users
  2. Add this line to the end of the file:
    export PATH="$HOME/bin:$PATH"
  3. Apply the changes:
    source ~/.bashrc # or source ~/.zshrc for zsh users
3. Verify Installation:
  1. Run the following command to verify the Arduino CLI is installed:
    arduino-cli version
  2. You should see a version number if the installation was successful.
    Install the ESP32 Core
1. Update the Core Index: You need to add the ESP32 core to your Arduino CLI configuration. Run the following command to add the Espressif Systems package URL:
  arduino-cli config init
  arduino-cli config add board_manager.additional_urls https://raw.githubusercontent.com/espressif/arduino-esp32/gh-pages/package_esp32_index.json
2. Install the ESP32 Core: After adding the URL, install the ESP32 core using the following command:
  arduino-cli core update-index
  arduino-cli core install esp32:esp32
### Select the Correct Board
Now that you’ve installed the ESP32 core, you need to select the correct board variant for your ESP32-WROOM module. The most commonly used option for ESP32-WROOM is esp32:esp32:esp32.
1. List Available ESP32 Boards: To list all available ESP32 boards, run the following command:
  arduino-cli board listall
2. Choose the ESP32-WROOM Board: In most cases, you can use the esp32:esp32:esp32 board. So, when compiling and uploading your code, you would specify this board as the Fully Qualified Board Name (FQBN).
### Step 3: Compile and Upload for ESP32-WROOM
Once you’ve identified the board and installed the ESP32 core, you can compile and upload your sketch to the ESP32-WROOM as follows:
1. Compile the Sketch: Navigate to the directory of your Arduino sketch and compile it for the ESP32-WROOM:
  arduino-cli compile --fqbn esp32:esp32:esp32 /path/to/your/sketch
2. Upload the Sketch: After compiling, upload the sketch to the ESP32-WROOM:
  arduino-cli upload -p /dev/ttyUSB0 --fqbn esp32:esp32:esp32 /path/to/your/sketch
### Example Commands
If your sketch is in /home/user/my_esp32_project/, here’s how you would compile and upload:

cd /home/user/my_esp32_project/

# Compile the sketch for ESP32-WROOM
arduino-cli compile --fqbn esp32:esp32:esp32 .

# Upload the sketch to the ESP32-WROOM
arduino-cli upload -p /dev/ttyUSB0 --fqbn esp32:esp32:esp32 .